## Slide 1
Nuclear Hydrogen Production
Cátia Ribeiro | 110962
Fábio Costa | 108090
Margarida Cavaleiro | 110886
Pedro Manuel | 96303
Nuclear Hydrogen Production

## Slide 2: Members
Cátia Ribeiro
Margarida Cavaleiro
Fábio Costa
Pedro Manuel

## Slide 3: Agenda
Introduction
Nuclear Energy Applied to the Hydrogen Production
Future perspectives
Economic Analysis
Theoretical Fundamentals
Fig1: Schematic of Nuclear H2 production

## Slide 4: Introduction
Current Climate Context, Importance of H2 in Our Economy, Introduction to Nuclear H2
1

## Slide 5: Introduction
As such the demand is incresing rapidly according to “The Global Hydrogen Review” from 2024, the Global hydrogen demand reached 97 Mt in 2023, an increase of 2.5% compared to 2022
The disadvantage being that almost all hydrogen today is made from carbon-based materials, with significant CO2 emissions
So we need to make a shift to low-emission hydrogen production
IEA in 2023, https://www.iea.org/data-and-statistics/charts/global-hydrogen-demand-in-the-net-zero-scenario-2022-2050
Fig 2: Global hydrogen demand in the Net Zero Scenario 2022-2050

## Slide 6: Theoretical Fundamentals
Nuclear Energy, Hydrogen Production
2

## Slide 7: Hydrogen Colors
Incer-Valverde, J., Korayem, A., Tsatsaronis, G., & Morosuk, T. (2023). “Colors” of hydrogen: Definitions and carbon intensity. Energy Conversion and Management, 291, 117294
Fig 3: Hydrogen Colors

## Slide 8: Hydrogen Colors
Incer-Valverde, J., Korayem, A., Tsatsaronis, G., & Morosuk, T. (2023). “Colors” of hydrogen: Definitions and carbon intensity. Energy Conversion and Management, 291, 117294.
Fig 4: Worldwide plans for Hydrogen production

## Slide 9: Nuclear Energy
Nuclear power generation has existed since the 1960s, seeing massive growth globally
Nuclear power plants operate in 32 countries
Has a very high capacity factor
Its a baseload energy source
No energy source is completelly safe, but there have been improvements in research
Fig 5: Nuclear Power Generation, by Our World in Data for 2023

## Slide 10: Why should we produce nuclear hydrogen ?
Necessity of production from a source that is not so pollutant – low carbon emission projects
High demands of hydrogen in the future
Needs of a non intermittent hydrogen production
Fig 6. Comparison of the emissions intensity of different hydrogen production routes, 2022 from the Global Hydrogen Report 2024.

## Slide 11: Nuclear Energy for H2 Production
Water Electrolysis Using Nuclear Energy, High Temperature Thermolysis, Thermochemical Processes
3

## Slide 12: Methods
Fig 7:R. Walker, P. Sabharwall, J. Hartvigsen, and J. O’Brien, “Comparative review of hydrogen production technologies for nuclear hybrid energy systems,” Progress in Nuclear Energy, 2020.
→ Electrolysis
→ Thermochemical processes
→ Thermolysis

## Slide 13: Electrolysis
Fig 9: Scheme of a HTE unit using nuclear energy
S. . Fujiwara,et al, “Hydrogen production by high temperature electrolysis with nuclearreactor,” Progress in Nuclear Energy, 2008
Fig 8: Solid Oxide Electrolyser scheme
R. Walker, P. Sabharwall, J. Hartvigsen, and J. O’Brien, “Comparative review of hydrogen production technologies for nuclear hybrid energy systems,” Progress in Nuclear Energy, 2020.

## Slide 14
Thermochemical
S-I Cycle
✓ Large Scale production
✓ Competetive Cost
✓ High Efficiency
✗ Uncertainties in chemical kinetics
✗ Iodine availability
R. Walker, P. Sabharwall, J. Hartvigsen, and J. O’Brien, “Comparative review of hydrogen production technologies for nuclear hybrid energy systems,” Progress in Nuclear Energy, 2020.
Fig 10: Sulfur Iodine cycle

## Slide 15
Thermochemical
HyS Cycle
✓ 1/3 of the electric power required for Electrolysis
✗ SO2 crossover → improve catalysts
✗ Long term stable operation
Fig 11: Hybrid Sulfur cycle
R. Walker, P. Sabharwall, J. Hartvigsen, and J. O’Brien, “Comparative review of hydrogen production technologies for nuclear hybrid energy systems,” Progress in Nuclear Energy, 2020.

## Slide 16: Reactors for H2 production
Fig 12: Joel Guidez, in Fast Reactors, 2023
High-Temperature Gas-Cooled Reactors
Advanced Pressurized Water Reactor
Fig 13: Schematic of the PWR power plant, 2023

## Slide 17: Economic Analysis
Hydrogen Economic Evaluation Program (HEEP)
5

## Slide 18: HEEP parameters
Fig 14: Categories of input parameters
Fig 15: Technical input parameters
Fig 16: Main cost parameters
I. K. R.S. El-Emam, “International collaboration in the iaea nuclear hydrogen production program forbenchmarking of heep,” International Journal of Hydrogen Energy, vol. 42, pp. 3566–3571, 2017.

## Slide 19: Objectives
Examine the impact of production scale on the cost of nuclear hydrogen production
Compare nuclear hydrogen production cost with non-nuclear options
Determining the cost of hydrogen production

## Slide 20: System description
Fig 17: Layout of the hydrogen production, storage and transportation system
Advanced Pressurized Water (APWR)
High-Temperature Gas-Cooled (HTGR)
Conventional low temperature (CE)
High temperature (HTSE)
Reactors
Electrolysis technologies
A. A. Alabbadi, O. A. Obaid, and A. A. AlZahrani, “A comparative economic study of nuclear hydrogen production, storage, and transportation,” International Journal of Hydrogen Energy, vol. 54, pp. 849–863,2024

## Slide 21: Results
Fig 18: Nuclear hydrogen production parameters for 4 cases
Fig 19: Hydrogen production cost for the different cases and storage options
A. A. Alabbadi, O. A. Obaid, and A. A. AlZahrani, “A comparative economic study of nuclear hydrogen production, storage, and transportation,” International Journal of Hydrogen Energy, vol. 54, pp. 849–863,2024

## Slide 22: Results
Fig 20: Distribution of hydrogen production cost for the different cases
A. A. Alabbadi, O. A. Obaid, and A. A. AlZahrani, “A comparative economic study of nuclear hydrogen production, storage, and transportation,” International Journal of Hydrogen Energy, vol. 54, pp. 849–863,2024

## Slide 23: Results
Fig 21: Hydrogen production by electrolysis using different energy sources
Fig 22: Hydrogen production cost for the different sources
A. A. Alabbadi, O. A. Obaid, and A. A. AlZahrani, “A comparative economic study of nuclear hydrogen production, storage, and transportation,” International Journal of Hydrogen Energy, vol. 54, pp. 849–863,2024

## Slide 24: Future Perspective
Challenges and Advantages, Nuclear Hydrogen Demonstration Projects
6

## Slide 25: Challenges and Advantages
ICAN. (n.d.). The road to a world free of nuclear weapons. International Campaign to Abolish Nuclear Weapons
Clean production
Large-scale hydrogen generation
Multiple production methods
Main Advantages of Nuclear Hydrogen Production
High investments at long term to become operational
Public acceptance issues (safety, radioactive waste)
Need for advanced infrastructure and technical expertise
Main Obstacles of Nuclear Hydrogen Production
• Global opinions and environmental concerns shape nuclear strategies
• Varied national responses to the Fukushima accident
• Pro-nuclear arguments focus on safety and climate change benefits
• Anti-nuclear protests influence policies, especially in democracies

## Slide 26: Nuclear hydrogen demonstration projects
Fig 23: World map of Nuclear Hydrogen production projects

## Slide 27: Nuclear hydrogen demonstration projects
Using the High-Temperature Engineering Test Reactor (HTTR)
to establish HTGR technology and heat utilization technology
Project created by the Japan Atomic Energy Agency
Fig 24: News from the Nikkei Asia, 2024, https://asia.nikkei.com/Business/Energy/Japan-eyes-hydrogen-production-using-next-gen-nuclear-reactor

## Slide 28: Conclusion
Summary and Potentials
7

## Slide 29: Conclusion
Combining nuclear and renewable energy systems to co-produce electricity and hydrogen will help meet market demand;
High Temperature Electrolysis and Thermochemical processes are the most promising technologies ;
The production of hydrogen using nuclear energy should be specifically mentioned in hydrogen plans as a zero-carbon pathway, with defined targets and indications for its achievement;
We need to accept that nuclear is a reality and should take advantage of that to decarbonize other sectors.

## Slide 30: Thank you for your attention!

## Slide 31: Bibliography
S. Fujiwara, S. Kasai, H. Yamauchi, K. Yamada, S. Makino, K. Matsunaga, M. Yoshino, T. Kameda,T. Ogawa, S. Momma, and E. Hoashi, “Hydrogen production by high temperature electrolysis with nuclearreactor,” Progress in Nuclear Energy, vol. 50, no. 2, pp. 422–426, 2008.
R. Walker, P. Sabharwall, J. Hartvigsen, and J. O’Brien, “Comparative review of hydrogen productiontechnologies for nuclear hybrid energy systems,” Progress in Nuclear Energy, vol. 123, p. 103317, 05 2020.
K. R.S. El-Emam, “International collaboration in the iaea nuclear hydrogen production program forbenchmarking of heep,” International Journal of Hydrogen Energy, vol. 42, pp. 3566–3571, 2017.
A. A. Alabbadi, O. A. Obaid, and A. A. AlZahrani, “A comparative economic study of nuclear hydrogen production, storage, and transportation,” International Journal of Hydrogen Energy, vol. 54, pp. 849–863,2024
Incer-Valverde, J., Korayem, A., Tsatsaronis, G., & Morosuk, T. (2023). “Colors” of hydrogen: Definitions and carbon intensity. Energy Conversion and Management, 291, 117294.
Global hydrogen demand in the Net Zero Scenario, 2022-2050, by IEA in 2023, https://www.iea.org/data-and-statistics/charts/global-hydrogen-demand-in-the-net-zero-scenario-2022-2050
IEA in 2023, https://www.iea.org/data-and-statistics/charts/global-hydrogen-demand-in-the-net-zero-scenario-2022-2050